Contactless hunter registration
Radio Frequency Identity (RFID)
Or
Near Field Communication (NFC)

---
Motivation
- Existing punchers (9 pin connectors) are prone to damage due to hunters’ in a hurry
- Finding the correct way to plug the puncher takes time, unless it is known prior
- Guestimated 10 seconds can be saved if moved to contactless hunter registration without damage to equipment

---
Existing Hardware
- Fox & PRAL
  - PIC16F88
  - 18 pin, uses UART to talk to Puncher
  - Free pins: 1, 7, 9, none fully compatible to make use of a new UART, I2C or SPI.
- Puncher
  - PIC12F635
  - Too few pins in use, even difficult to connect to a debugger
- RS 232 DB9 connector
  - Non standard pins
  - (although RS 232 is only a recommended standard)

---
Approach 1:
Reuse Existing Hardware
- The existing hardware is highly customized/optimized for the task at hand.
- Adding new features could be difficult unless lots of physical rewiring and software driven protocols
- High impact for failure when new items such as RFID is included in the system.
- High development effort and impact on the existing system

---
Approach 2: Use Arduino with RFID/NFC capability
$2.50
$25
1 uA (standby)
Fox
Arduino
RFID Hunter tag
PN532
RFID Reader
$40
RFID: https://www.fasttech.com/product/1200002-rewritable-programmable-nxp-mifare-nfc-tag-keychai
Need a cheaper way to source these items: aliexpress?
Wireless

---
Approach 2: Use Arduino with RFID/NFC capability
- No impact on the existing system
- Requires additional external MCU (Arduino Uno based)
- A standalone system also possible
  - Requires external battery
  - With real time clock (RTC): it can maintain its own clock, presynchronized via USB programming via computer
- When connected to the DB9 connector to the fox, the fox can also register and behave like in the existing system
- Low impact on the existing fox programming
- Puncher will be a passive RFID/NFC where it can also keep track of the hunter time.
- Values from the NFC based puncher can be read using any other NFC enabled device, such as a modern mobile phone.
- 3D printed case to shelter the Arduino and RFID reader

---
Approach 2: Other benefits
Generic hardware: easily replaced with off the shelf components, no real hardware-rework needed. All software tools are open source, and nearly anyone can program.
- The punchers can be used for other orienteering events apart from Fox Hunting, as they can function in standalone mode.
- The Arduinos can be used for personal projects when fox hunting is not anytime soon.
- Future use-case:
  - Arduino’s UART can be used to connect LoRa (Long Range Radio in ISM band) which can form a network.
  - The organizer himself can track all the hunter registrations.
  - Morse coded signals can be sent. Need to explore.
- In case the prototyping goes wrong, the components can be reused.

---
Approach 3: Use customized hardware

---
Need to do
- Perform analysis of the signals over the DB9 connector to the puncher using logic analyzer.